## Slide 1: ECE 411 Spring 2016 Lecture 9
Branch Prediction

## Slide 2: Types of Branches

## Slide 3: Static Branch Prediction
Uni-directional, always predict taken (or not taken)
Backward taken, Forward not taken
  Need offset information (when?)
Compiler hints with branch annotation
  When the info will be available? Post-decode?

## Slide 4: Why branches are predictrable?
Correlation
B1: if (x)
...
B2: if (y)
...
z=x&&y
B3: if (z)
...
B3 can be predicted with 100% accuracy based on the outcomes of B1 and B2

## Slide 5: Patterns for all three branches
000, 100, 010, 111
  00 à 0
  01 à 0
  10 à 0
  11 à 1
If the history is 000 100 010 11
  What is the prediction?

## Slide 6: Simplest Dynamic Branch Predictor
Prediction based on latest outcome
Index by some bits in the branch PC
  Aliasing
T
NT
T
T
NT
NT
.
.
.
for (i=0; i<100; i++) {
….
}
addi r10, r0, 100
addi r1, r1, r0
L1:
… …
… …
addi r1, r1, 1
bne r1, r10, L1
… …
0x40010100
0x40010104
0x40010108
…
0x40010A04
0x40010A08
How accurate?
NT
T
1-bit
Branch
History
Table

## Slide 7: FSM of the Simplest Predictor
A 2-state machine
Change mind fast
0
1
If branch not taken
If branch taken
0
1
Predict not taken
Predict taken

## Slide 8: Example using 1-bit branch history table
for (i=0; i<4; i++) {
….
}
0
Pred
Actual
T
T

1
1

T
T

1
1
addi r10, r0, 4
addi r1, r1, r0
L1:
… …
addi r1, r1, 1
bne r1, r10, L1
NT
0


T
1

T

1

T
T

1
1
NT
0

T
1

60% accuracy

## Slide 9: 2-bit Saturating Up/Down Counter Predictor
Not Taken
Taken
Predict Not taken
Predict taken
ST: Strongly Taken
WT: Weakly Taken
WN: Weakly Not Taken
SN: Strongly Not Taken
01/
WN
00/
SN
10/
WT
11/
ST
MSB: Direction bit
LSB: Hysteresis bit

## Slide 10: Example using 2-bit up/down counter
for (i=0; i<4; i++) {
….
}
01
Pred
Actual
T
T

10
11

T
T

11
11
addi r10, r0, 4
addi r1, r1, r0
L1:
… …
addi r1, r1, 1
bne r1, r10, L1
NT
10


T
11

T

11

T
T

11
11
NT
10

T
1

80% accuracy

## Slide 11: Typical Table Organization
Hash
PC (32 bits)
.
.
.
.
.
2N entries
Prediction
N bits
FSM
Update
Logic
table update
Actual outcome

## Slide 12: Simplest Dynamic Branch Predictor
T
NT
T
T
NT
NT
.
.
.
addi r10, r0, 100
addi r1, r1, r0
L1:
add r21, r20, r1
lw r2, (r21)
beq r2, r0, L2
… …
j L3
L2:
… … …
L3:
addi r1, r1, 1
bne r1, r10, L1
0x40010100
0x40010104
0x40010108
0x4001010c
0x40010110
0x40010210
0x40010B0c
0x40010B10
for (i=0; i<100; i++) {
if (a[i] == 0) {
…
}
…
}
NT
T
1-bit
Branch
History
Table

## Slide 13: Special Branches
Procedure calls and returns
  Calls are always taken
  Return address almost always known
Return Address Stack (RAS)
  On a procedure call, push the address of the instruction after the call onto the stack

## Slide 14: Types of Branches

## Slide 15: Branch Target Buffers
Predict the location of branches in the instruction stream
Predict the destination of branches

## Slide 16: BTB Operation
Use PC (all bits) for lookup
  Match implies this is a branch
If match and predict bits: taken, set PC to predicted PC
If branch predict wrong: must recover (same as branch hazards we’ve already seen)
If decode indicates branch w/ no BTB match, two choices:
  look up prediction now and act on it
  just predict not taken
When branch resolved, update BTB (at least prediction bits, maybe more)

## Slide 17: BTB Performance
Two things that can go wrong
  Didn’t predict the branch (misfetch)
  Mispredicted a branch (mispredict)
Suppose BTB hit rate of 85% and predict accuracy of 90%, misfetch penalty of 2 cycles and mispredict penalty of 10 cycles, what is average branch penalty?
Can use both BTB and branch predictor
  Have no prediction bits in BTB (why is that a good idea?)
  Presence of PC in BTB indicates a lookup in branch predictor to predict whether the branch will go to destination address in BTB

## Slide 18: Types of Branches

## Slide 19: What about indirect jumps/returns?
Branch predictor does really well with conditional jumps
BTB does really well with unconditional jumps (jump, jal, etc.)
Indirect jumps often jump to different destinations, even from the same instruction. Indirect jumps most often used for return instructions.
Return easily handled by a stack.
  jal -> push PC+4
  return -> predict jump to address on top of stack, pop stack

## Slide 20: Instruction Fetch Stage
PC
Instruction Memory (i-Cache)
+ 4
PHT
MUX
Next PC Logic
Hit/miss
T/NT
Branch
Execution
T/NT
BTB
Branch
Execution
Address

## Slide 21: Update PHT and BTB (Prediction Miss)
PC
Instruction Memory (i-Cache)
PHT
MUX
BTB
Branch PC
Target PC